## Slide 1: DMA-API & CMA ,IOMMU INTEGRATION
By
Vijayanand

## Slide 2
Memory
Access

## Slide 3
1
2
(1) CPU writes to memory
(2) Device reads from memory
Memory
Device
Memory
Controller
CPU Core
Simple case

## Slide 4
2
1
3
(1)
(2) (3)
CPU writes to memory
CPU flushes its write buffers
Device reads from memory
Memory
Device
Memory
Controller
CPU Core
Write Buffer

## Slide 5
2
L1
Cache
1
3
(1)
(2) (3)
CPU writes to memory
CPU cleans L1 cache
Device reads from memory
Memory
Device
Memory
Controller
CPU Core
L1 Cache

## Slide 6
3
4
2
1
(1)
(2) (3)
(4)
CPU writes to memory
CPU cleans L1 cache
CPU cleans L2 cache
Device reads from memory
Memory
Device
Memory
Controller
CPU L1
Core Cache
L2 Cache
CPU L1
Core Cache
L2 Cache

## Slide 7
2
Controller
1
(1) CPU writes to memory
(2) Device reads from memory
Cache Coherent
Interconnect
Memory
Memory
Device
CPU L1
Core Cache
L2 Cache
CPU L1
Core Cache
Cache Coherent Interconnect

## Slide 8
2
3
Controller
1
(1)
(2) (3)
CPU writes to memory
CPU programs the IOMMU Device reads from memory
Cache Coherent
Interconnect
IOMMU
Memory
Memory
Device
CPU L1
Core Cache
L2 Cache
CPU L1
Core Cache
IOMMU

## Slide 9
Memory
Mapping

## Slide 10
Fully Coherent
●
Coherent (or consistent) memory is memory for which a write by either the device or the processor can immediately be read by the processor or device without having to worry about caching effects.
Consistent memory can be expensive on some platforms, and the minimum allocation length may be as big as a page.

## Slide 11
Write Combining
●
Writes to the mapping may be buffered to improve performance. You need to make sure to flush the processor's write buffers before telling devices to read that memory. This memory type is typically used for (but not restricted to) graphics memory.

## Slide 12
Weakly Ordered
●
Reads and writes to the mapping may be weakly ordered, that is that reads and writes may pass each other. Not all architectures support non-cached weakly ordered mappings.

## Slide 13
Non-Coherent
●
This memory mapping type permits speculative reads, merging of accesses
and (if interrupted by an exception) repeating of writes without side effects.
Accesses to non-coherent memory can always be buffered, and in most situations they are also cached (but they can be configured to be uncached).
There is no implicit ordering of non-coherent memory accesses.
When using non-coherent memory mappings you are guaranteeing to the
platform that you have all the correct and necessary sync points for this
memory in the driver.

## Slide 14
DMA
Mapping
API

## Slide 15: Operations of DMA Mapping API
Allocate memory suitable for DMA operations
Map DMA memory to devices
Synchronize memory between CPU and device domains

## Slide 16
#include
<linux/dma-mapping.h>
DMA Mapping API

## Slide 17: Coherent DMA allocations
This routine allocates a region of <size> bytes of consistent memory.
It returns a pointer to the allocated region (in the processor's virtual address space) or NULL if the allocation failed.
It also returns a <dma_handle> which may be cast to an unsigned integer the same width as the bus and given to the device as the bus address base of the region.
A driver can allocate coherent memory with a call to dma_alloc_coherent:
void * dma_alloc_coherent (struct device *dev, size_t size,
dma_addr_t *dma_handle, gfp_t flag);
Notes: These mappings usually exist for the life of the driver.
A coherent buffer must be simultaneously available to both the CPU and the peripheral (other types of mappings, as we will see later, can be available only to one or the other at any given time).
As a result, coherent mappings must live in cache-coherent memory.
Coherent mappings can be expensive to set up and use.
This function handles both the allocation and the mapping of the buffer.
The first two arguments are the device structure and the size of the buffer needed.
The function returns the result of the DMA mapping in two places. The return value from the function is a kernel virtual address for the buffer, which may be used by the driver; the associated bus address, meanwhile, is returned in dma_handle.

## Slide 18
void dma_free_coherent (struct device *dev, size_t size,
void *cpu_addr, dma_addr_t dma_handle);
When the buffer is no longer needed (usually at module unload time), it should be returned to the system with dma_free_coherent:
Coherent DMA allocations
Note: The minimum allocation length may be as big as a page.

## Slide 19: DMA Pools
If your driver needs lots of smaller memory regions,you can use the dma_pool API to do that. ( #include <linux/dmapool.h> )
Create a DMA pool :
struct dma_pool * dma_pool_create(const char *name, struct device *dev,
size_t size, size_t align, size_t boundary);
Allocate memory from DMA pool :
void *dma_pool_alloc (struct dma_pool *pool, gfp_t mem_flags,
dma_addr_t *handle);
Notes: Here, name is a name for the pool, dev is your device structure, size is the size of the buffers to be allocated from this pool, align is the required hardware alignment for allocations from the pool (expressed in bytes), and allocationis, if nonzero, a memory boundary that allocations should not exceed

## Slide 20: DMA Pools
Free memory allocated from DMA pool :
void dma_pool_free(struct dma_pool *pool, void *vaddr, dma_addr_t addr);
Destroy DMA pool :
void dma_pool_destroy(struct dma_pool *pool);

## Slide 21
void *
dma_alloc_attrs(struct device *dev, size_t size,
dma_addr_t *dma_handle, gfp_t flag,
struct dma_attrs *attrs);
void
dma_free_attrs(struct device *dev, size_t size,
void *cpu_addr, dma_addr_t dma_handle, struct dma_attrs *attrs);
Those two functions extend the coherent memory allocation API by allowing the caller to specify attributes for the allocated memory. When attrs is NULL the behaviour is identical to the dma_*_coherent() functions.
Attribute-Based Allocation

## Slide 22
DMA_ATTR_WRITE_COMBINE
DMA_ATTR_WEAK_ORDERING
DMA_ATTR_NON_CONSISTENT
DMA_ATTR_WRITE_BARRIER
DMA_ATTR_FORCE_CONTIGUOUS
DMA_ATTR_NO_KERNEL_MAPPING
DMA_ATTR_SKIP_CPU_SYNC
All
attributes are optional. An architecture that doesn't
implement an attribute
ignores it and exhibit default behaviour.
(See Documentation/DMA-attributes.txt)
DMA Mapping Attributes

## Slide 23: DMA Mask
int dma_set_mask(struct device *dev, u64 mask),
int dma_set_coherent_mask(struct device *dev, u64 mask);
int dma_set_mask_and_coherent(struct device *dev, u64 mask);
Many devices are limited in the range of memory they can address, for a number of reasons.
By default, the kernel assumes that your device can perform DMA to any 32-bit address.
If this is not the case, you should inform the kernel of that fact with a call to:
Notes: The mask should show the bits that your device can address; if it is limited to 24 bits, for example, you would pass mask as 0x0FFFFFF.
The return value is nonzero if DMA is possible with the given mask; if dma_set_mask returns 0, you are not able to use DMA operations with this device.

## Slide 24: Streaming DMA Mappings
These mappings expect to work with a buffer that has already been allocated by the driver.
Memory that is DMA’ble :
Memory allocated by page allocator(i.e. __get_free_page*()) or the generic memory allocators(i.e. kmalloc() or kmem_cache_alloc()) .
Buffers used for DMA must be cacheline-aligned.

## Slide 25: DMA Direction
When setting up a streaming mapping, you must tell the kernel in which direction the data is moving.
enum dma_data_direction {
DMA_BIDIRECTIONAL = 0,
DMA_TO_DEVICE = 1,
DMA_FROM_DEVICE = 2,
DMA_NONE = 3,
};

## Slide 26
dma_addr_t
dma_map_single_attrs(struct device *dev, void *ptr, size_t size,
enum dma_data_direction dir,
struct dma_attrs *attrs);
void
dma_unmap_single_attrs(struct device *dev, dma_addr_t addr,
size_t size, enum dma_data_direction dir,
struct dma_attrs *attrs);
dma_addr_t dma_map_single(...);
void dma_unmap_single(...);
DMA Streaming Mapping

## Slide 27
Some important rules apply to streaming DMA mappings:
The buffer must be used only for a transfer that matches the direction value given when it was mapped.
Once a buffer has been mapped, it belongs to the device, not the processor. Until the buffer has been unmapped, the driver should not touch its contents in any way. Only after dma_unmap_single has been called is it safe for the driver to access the contents of the buffer (with one exception that we see shortly)..
The buffer must not be unmapped while DMA is still active, or serious system instability is guaranteed.
Notes: There are actually two reasons why this rule makes sense. First, when a buffer is mapped for DMA, the kernel must ensure that all of the data in that buffer has actually been written to memory. It is likely that some data is in the processor's cache when dma_unmap_single is issued, and must be explicitly flushed. Data written to the buffer by the processor after the flush may not be visible to the device
Second, consider what happens if the buffer to be mapped is in a region of memory that is not accessible to the device. Some architectures simply fail in this case, but others create a bounce buffer. The bounce buffer is just a separate region of memory that is accessible to the device. If a buffer is mapped with a direction of DMA_TO_DEVICE, and a bounce buffer is required, the contents of the original buffer are copied as part of the mapping operation. Clearly, changes to the original buffer after the copy are not seen by the device. Similarly, DMA_FROM_DEVICE bounce buffers are copied back to the original buffer by dma_unmap_single; the data from the device is not present until that copy has been done.
Incidentally, bounce buffers are one reason why it is important to get the direction right. DMA_BIDIRECTIONAL bounce buffers are copied both before and after the operation, which is often an unnecessary waste of CPU cycles

## Slide 28
dma_addr_t
dma_map_page(struct device *dev, struct page *page, size_t offset, size_t size , enum dma_data_direction dir);
Single-page Streaming Mapping
void
dma_unmap_page(struct device *dev, dma_addr_t addr,
size_t size, enum dma_data_direction dir);

## Slide 29
int
dma_map_sg(struct device *dev, struct scatterlist *sg, int nents, enum dma_data_direction dir);
void
dma_unmap_sg(struct device *dev, struct scatterlist *sg, int nents,
enum dma_data_direction dir);
Scatter/Gather Mapping
After mapping, the output address (the one you give to the device) can be obtained with
dma_addr_t sg_dma_address(struct scatterlist *sg);
and the length can be obtained with
unsigned int sg_dma_len(struct scatterlist *sg);
Notes: Suppose you have several buffers, all of which need to be transferred to or from the device. This situation can come about in several ways, including from a readv or writev system call, a clustered disk I/O request, or a list of pages in a mapped kernel I/O buffer. You could simply map each buffer, in turn, and perform the required operation, but there are advantages to mapping the whole list at once.
On such systems with IOMMUS , physically discontiguous pages can be assembled into a single, contiguous array from the device's point of view.
it can turn multiple operations into a single DMA, and speed things up accordingly.
Finally, if a bounce buffer must be used, it makes sense to coalesce the entire list into a single buffer (since it is being copied anyway).
The first step in mapping a scatterlist is to create and fill in an array of struct scatterlist describing the buffers to be transferred.
where nents is the number of scatterlist entries passed in. The return value is the number of DMA buffers to transfer; it may be less than nents.
As part of that task, it also coalesces buffers that are adjacent to each other in memory.
If the system your driver is running on has an I/O memory management unit, dma_map_sg also programs that unit's mapping registers, with the possible result that, from your device's point of view, you are able to transfer a single, contiguous buffer.

## Slide 30
int
dma_mapping_error(struct device *dev, dma_addr_t dma_addr);
In some circumstances dma_map_*() will fail to create a mapping. A driver can check for these errors by testing the returned DMA address with dma_mapping_error(). A non-zero return value means the mapping could not be created and the driver should take appropriate action
Error Checking

## Slide 31
void
dma_sync_single_for_cpu(struct device *dev,
dma_addr_t addr, size_t size, enum dma_data_direction dir);
Synchronization
void
dma_sync_single_for_device(struct device *dev, dma_addr_t addr, size_t size, enum dma_data_direction dir);
Notes: keeping mapping around and giving ownership to components ,component having ownership can access , other wise caching issues

## Slide 32
Synchronization
void dma_sync_single_range_for_*(struct device *dev, dma_addr_t addr,
unsigned long offset, size_t size,enum dma_data_direction dir);
void dma_sync_sg_for_*(struct device *dev, struct scatterlist *sg, int nelems,
enum dma_data_direction dir);
(* = cpu or device)
Notes: sync range only sync small piece of buffer

## Slide 33
Usage
my_card_setup_receive_buffer(struct my_card *cp, char *buffer, int len)
{
dma_addr_t mapping;
mapping = dma_map_single(cp->dev, buffer, len, DMA_FROM_DEVICE);
if (dma_mapping_error(cp->dev, dma_handle)) {
/*
* reduce current DMA mapping usage,
* delay and try again later or
* reset driver.
*/
goto map_error_handling;
}
cp->rx_buf = buffer;
cp->rx_len = len;
cp->rx_dma = mapping;
give_rx_buf_to_card(cp);
}
Notes: sync range only sync small piece of buffer

## Slide 34
Usage
my_card_interrupt_handler(int irq, void *devid, struct pt_regs *regs)
{
struct my_card *cp = devid;
...
if (read_card_status(cp) == RX_BUF_TRANSFERRED) {
struct my_card_header *hp;
/* Examine the header to see if we wish
* to accept the data. But synchronize
* the DMA transfer with the CPU first
* so that we see updated contents.
*/
dma_sync_single_for_cpu(&cp->dev, cp->rx_dma,
cp->rx_len,
DMA_FROM_DEVICE);
/* Now it is safe to examine the buffer. */
hp = (struct my_card_header *) cp->rx_buf;
if (header_is_ok(hp)) {
dma_unmap_single(&cp->dev, cp->rx_dma, cp->rx_len,
DMA_FROM_DEVICE);
pass_to_upper_layers(cp->rx_buf);
make_and_setup_new_rx_buf(cp);
} else {
/* CPU should not write to
* DMA_FROM_DEVICE-mapped area,
* so dma_sync_single_for_device() is
* not needed here. It would be required
* for DMA_BIDIRECTIONAL mapping if
* the memory was modified.
*/
give_rx_buf_to_card(cp);
}
}
}
Notes: sync range only sync small piece of buffer

## Slide 35
Handling Error
dma_addr_t dma_handle;
dma_handle = dma_map_single(dev, addr, size, direction);
if (dma_mapping_error(dev, dma_handle)) {
/*
* reduce current DMA mapping usage,
* delay and try again later or
* reset driver.
*/
goto map_error_handling;
}
Notes: sync range only sync small piece of buffer

## Slide 36
Note
1) Struct scatterlist requirements.
Don't invent the architecture specific struct scatterlist; just use
<asm-generic/scatterlist.h>. You need to enable
CONFIG_NEED_SG_DMA_LENGTH if the architecture supports IOMMUs
(including software IOMMU).
2) ARCH_DMA_MINALIGN
Architectures must ensure that kmalloc'ed buffer is
DMA-safe. Drivers and subsystems depend on it. If an architecture
isn't fully DMA-coherent (i.e. hardware doesn't ensure that data in
the CPU cache is identical to data in main memory),
ARCH_DMA_MINALIGN must be set so that the memory allocator
makes sure that kmalloc'ed buffer doesn't share a cache line with
the others. See arch/arm/include/asm/cache.h as an example.
Note that ARCH_DMA_MINALIGN is about DMA memory alignment
constraints. You don't need to worry about the architecture data
alignment constraints (e.g. the alignment constraints about 64-bit
objects).
Notes: sync range only sync small piece of buffer

## Slide 37
struct dma_map_ops
arm_dma_ops
iommu_ops
CMA allocator
arch/arm/mm/dma-mapping.c
Abstraction of IOMMU and CMA under DMA API
struct device
removed_ops
struct dma_map_ops removed_dma_ops = {
.alloc = removed_alloc,
.free = removed_free,
.mmap = removed_mmap,
.map_page = removed_map_page,
.unmap_page = removed_unmap_page,
.map_sg = removed_map_sg,
.unmap_sg = removed_unmap_sg,
.sync_single_for_cpu = removed_sync_single_for_cpu,
.sync_single_for_device = removed_sync_single_for_device,
.sync_sg_for_cpu = removed_sync_sg_for_cpu,
.sync_sg_for_device = removed_sync_sg_for_device,
.remap = removed_remap,
.unremap = removed_unremap,
};
arch/arm/mm/dma-mapping.c
drivers/base/dma-removed.c

## Slide 38
CMA
Integration

## Slide 39
#include <linux/dma-contiguous.h>
CMA
CMA works by reserving memory early at boot time. This memory, called a CMA area or a CMA context, is later returned to the buddy allocator so that it can be used by regular applications. To do the reservation, one needs to call:
void dma_contiguous_reserve (phys_addr_t limit);
just after the low-level "memblock" allocator is initialized but prior to the buddy allocator setup. On ARM, for example, it is called in arm_memblock_init() .
To assign a CMA context to a device :
int dma_declare_contiguous (struct device *dev, unsigned long size, phys_addr_t base, phys_addr_t limit);
Notes: The limit argument specifies physical address above which no memory will be prepared for CMA. The intention is to limit CMA contexts to addresses that DMA can handle. In the case of ARM, the limit is the minimum of arm_dma_limit and arm_lowmem_limit. Passing zero will allow CMA to allocate its context as high as it wants. The only constraint is that the reserved memory must belong to the same zone.
The first argument of the function is the device that the new context is to be assigned to. The second specifies the size in bytes (not in pages) to reserve for the areas. The third is the physical address of the area or zero. The last one has the same meaning as dma_contiguous_reserve()'s limit argument. The return value is either zero or a negative error code.

## Slide 40
CMA Integration
To allocate CMA memory:
struct page *dma_alloc_from_contiguous(struct device *dev, int count, unsigned int align);
The return value is the first of a sequence of count allocated pages.
To free the allocated buffer:
bool dma_release_from_contiguous(struct device *dev, struct page *pages, int count);
If the region passed to the function did not come from CMA, the function will return false. Otherwise, it will return true.
Notes: Its first argument is a device that the allocation is performed on behalf of. The second specifies the number of pages (not bytes or order) to allocate. The third argument is the alignment expressed as a page order. It enables allocation of buffers whose physical addresses are aligned to 2align pages. To avoid fragmentation, if at all possible pass zero here. It is worth noting that there is a Kconfig option (CONFIG_CMA_ALIGNMENT) which specifies maximum alignment accepted by the function. Its default value is 8 meaning 256-page alignment.

## Slide 41
reserved-memory {
venus_fw_mem: venus_fw_region {
compatible = "shared-dma-pool";
alloc-ranges = <0x0 0x80000000 0x0 0x20000000> alignment = <0x0 0x400000>;
size = <0x0 0x800000>;
};
}
qcom,venus@cce0000 {
compatible = "qcom,pil-tz-generic";
reg = <0xcce0000 0x4000>;
.
.
memory-region = <&venus_fw_mem>;
status = "ok";
};

## Slide 42
“drivers/of/of_reserved_mem.c”
np = of_parse_phandle(dev->of_node, "memory-region", 0)
ret = rmem->ops->device_init(rmem, dev);

## Slide 43
"drivers/base/dma-contiguous.c"
RESERVEDMEM_OF_DECLARE(cma, "shared-dma-pool", rmem_cma_setup);
rmem->ops = &rmem_cma_ops;
static const struct reserved_mem_ops rmem_cma_ops = {
.device_init = rmem_cma_device_init,
.device_release = rmem_cma_device_release,
};
rmem_cma_device_init ()
dev_set_cma_area(dev, rmem->priv);

## Slide 44
dma_alloc_coherent
If (dev_get_cma_area(dev))
(device specific/default)
cma_allocator
dma_alloc_from_contiguous

## Slide 45
Carved out Regions
#include <linux/dma-removed.h>
reserved-memory {
modem_fw_mem: modem_fw_region@8ac00000 {
compatible = "removed-dma-pool";
no-map;
reg = <0x0 0x8ac00000 0x0 0x7e00000>;
};
};
pil_modem: qcom,mss@4080000 {
compatible = "qcom,pil-q6v55-mss";
reg = <0x4080000 0x100>,<0x1f63000 0x008>,
memory-region = <&modem_fw_mem>;
.
.
};

## Slide 46
"drivers/base/dma-removed.c"
RESERVEDMEM_OF_DECLARE(dma, "removed-dma-pool", removed_dma_setup);
rmem->ops = &removed_mem_ops;
static const struct reserved_mem_ops removed_mem_ops = {
.device_init = rmem_dma_device_init,
.device_release = rmem_dma_device_release,
};
rmem_dma_device_init()
set_dma_ops(dev, &removed_dma_ops)
dma_assign_removed_region(dev, mem);

## Slide 47
dma_alloc_coherent
ops->alloc
removed_alloc

## Slide 48
IOMMU
Integration

## Slide 49
#include <linux/iommu.h>
IOMMU API
struct iommu_domain * iommu_domain_alloc(struct bus_type *bus);
void iommu_domain_free(struct iommu_domain *domain);
int iommu_attach_device(struct iommu_domain *domain, struct device *dev);
void iommu_detach_device(struct iommu_domain *domain, struct device *dev);
int iommu_map(struct iommu_domain *domain,unsigned long iova, phys_addr_t paddr,
size_t size, int prot);
size_t iommu_unmap(struct iommu_domain *domain, unsigned long iova, size_t size);
Notes:   domain (which is really just a handle to some page tables),
  Contains data that SMMU driver uses to determine which SMMU you are trying to map into.
  A domain also has one or more virtual address space pools.
    Pools define the VA range
    Different pools in the same domain separates the different functionality
Creates a domain and allocates a first level page table
Turns on power to the SMMU (if power collapsible)
Votes for minimum bus bandwidth (on 8x10 and B-family)
Program the SMMU and enables translations in a context bank
Maps a virtual address to a physical address

## Slide 50
IOMMU Integration
struct dma_iommu_mapping * arm_iommu_create_mapping(struct bus_type *bus,
dma_addr_t base, size_t size);
Creates a mapping structure which holds information about used/unused IO address ranges, which is required to perform memory allocation and mapping with IOMMU aware functions.
int arm_iommu_attach_device(struct device *dev, struct dma_iommu_mapping *mapping);
Attaches specified IO address space mapping to the provided device . This replaces the dma operations (dma_map_ops pointer) with the IOMMU aware version.
void arm_iommu_detach_device(struct device *dev);
void arm_iommu_release_mapping (struct dma_iommu_mapping *mapping);
Notes: This allocates memory for your page table. If you're managing your own VA space (like the GPU driver) you'll actually use iommu_domain_alloc
This actually allocates memory for your page tables, programs some of the SMMU registers (TTBR0 and friends) and enables the context bank for translations (although there won't be much for it to do at the moment since you haven't mapped anything yet)

## Slide 51
ipa_hw: qcom,ipa@14780000 {
compatible = "qcom,ipa";
reg = <0x14780000 0x4effc>, <0x14784000 0x26934>;
reg-names = "ipa-base", "bam-base";
ipa_smmu_ap: ipa_smmu_ap {
compatible = "qcom,ipa-smmu-ap-cb";
iommus = <&anoc2_smmu 0x19C0>;
qcom,iova-mapping = <0x10000000 0x40000000>;
};
.
.
};
Notes: IPA : Internet Packet Accelerator

## Slide 52
arm_iommu_create_mapping iommu_domain_alloc
arm_iommu_attach_device iommu_attach_device
& sets dma_map_ops to iommu_ops
dma_alloc_coherent allocates memory
and calls iommu_map
"drivers/platform/msm/ipa/ipa_v3/ipa.c"
In ipa3_plat_drv_probe

## Slide 53: References
Linux Device Drivers , Chapter : 15
Documentation/DMA-API-HOWTO.txt
Documentation/DMA-API.txt
Documentation/DMA-attributes.txt
https://lwn.net/Articles/486301/