## Slide 1: Memory cgroups

## Slide 2: Agenda
Problems with conventional memcg
Per-app memcg
Problems with per-app memcg
Per-app memcg – Way Forward

## Slide 3: Conventional MEMCG – Issues
The first attempt with memcg - Creating memcg based on priority. i.e. one memcg each for foreground, background, services etc.
Movement of tasks from one memcg to other requires the charges to be moved (charge migration).
  Charge migration is slow and can take seconds depending on the size of task moved.
  Charge migration causes following issues
    RCU issues due to extensive usage of RCU writes
    Lock(cgroup_mutex) contention between CPU and memory cgroup transitions resulting in janks
    Launch latency impact
  Charge migration cannot be disabled as it results in memcgs being polluted with pages of tasks not belonging to the memcg.

## Slide 4: Per App Memcg
When these problems with MEMCG on Android was presented in LKML, Johannes Weiner suggested per-app cgroup.
Each process is put in its own memcg.
When the process has to be moved from say foreground to background, the processes' memcg controls are modified.
Thus, no charge migration.
Since task when spawned is by default part of root memcg, it is moved to it’s own memcg right after fork() before exec(), to reduce the memory charged to root memcg.

## Slide 5: MEMCG – Per app memcg - Improvements
These graphs indicate the improvement with per app memcg.
  Lock contentions are completely avoided
Chart: Phase 1 - memory cgroups
Chart: cpu_tx without memory cgroups
Chart: Per app memcg
memcg updates are taking ~ 100 to 150msec
cpu cgroup updates are almost < 1msec, but occasionally goes about 100 to 150msec
cpu cgroup updates are always < 0.5 msec
cpu cgroup updates are < 0.5 msec.
Memcg updates are < 0.5 msec.

## Slide 6: MEMCG – Per app memcg - Problems
Launch Latency– 2GB 64 bit.
Higher launch latency with per-app memcg

## Slide 7: MEMCG – Per app memcg - Problems
Vmstat indicates thrashing
The kswapd and direct reclaims are less, but 5x time is spent in kswapd and direct reclaim path and more pages are reclaimed.

## Slide 8: MEMCG – Per app memcg - Problems
Per-app model results in separate LRUs created per app and this results in very small sized LRUs.
The small size of LRUs result in these LRUs being skipped at scan priorities near to DEF_PRIORITY. This causes scan priority drop.
The scan priority drop results in excessive reclaim at lower priorities and thus more time spent in reclaim.
The presence of more number of LRUs results in more number of loops in the reclaim code (shrink_zone) for scanning each LRU. This results in higher CPU consumption.
Small LRUs result in pages being aged within their small LRUs and not on a global level and the result is thrashing.

## Slide 9: MEMCG – Per app memcg – Way forward
Another experiment was tried to reduce the number of per app cgroups by creating memcgs only for activity based tasks.
There was improvement, but the issue persists.
Soft reclaim was tried, but the interface is difficult to be used on Android because the size of apps varies and it is difficult to find the right value of soft reclaim thresholds.
Another change is being experimented where the page is linked to 2 LRUs. One global LRU and another LRU of its own (per app memcg LRU). This lets global reclaim use the global LRU and targeted reclaim can use per memcg LRU.
Kernel unit tests show improvement with this approach. But more experiments need to done to find the right way to use the per-app memcg LRU.

## Slide 10: Summary
The conventional way of grouping tasks based on priority using MEMCG has performance issues.
Per-app MEMCG seems to be a good alternative, but it creates problems in memory reclaim.
Dual LRU approach with per-app memcg seems to give good improvements.
  Improvements observed with kernel level tests
  This needs more testing and analysis
Dual LRU needs changes to reclaim code
  Need to involve community to review these changes or suggest alternative
  Google and QC can work together to finalize and upstream an acceptable solution with memcg

## Slide 11: Priority based reclaim with memcg
Key Stats | No MemCG | MemCG Priority (FG 10, Root 9, BG 0) | MemCG Priority (FG 5, Root 4, BG -5)
KSWAPD_S_AT_0 % reclaim | 0.0 | 0.0 | 0.0
KSWAPD_S_AT_1 % reclaim | 0.5 | 0.0 | 0.7
KSWAPD_S_AT_2 % reclaim | 5.3 | 32.7 | 10.3
KSWAPD_S_AT_3 % reclaim | 7.9 | 53.4 | 11.8
KSWAPD_S_AT_4 % reclaim | 11.3 | 4.1 | 10.8
KSWAPD_S_AT_5 % reclaim | 16.8 | 3.3 | 16.5
KSWAPD_S_AT_6 % reclaim | 22.1 | 2.5 | 16.4
KSWAPD_S_AT_7 % reclaim | 16.8 | 1.8 | 13.6
KSWAPD_S_AT_8 % reclaim | 9.3 | 1.1 | 10.7
KSWAPD_S_AT_9 % reclaim | 6.0 | 0.8 | 4.9
KSWAPD_S_AT_10 % reclaim | 2.3 | 0.1 | 2.3
KSWAPD_S_AT_11 % reclaim | 1.1 | 0.0 | 1.3
KSWAPD_S_AT_12 % reclaim | 0.5 | 0.0 | 0.7
Pgpgin | 153.66 | 390.98 | 308.18
Pgpgout | 2.47 | 2.48 | 2.52
pgpgoutclean | 152.58 | 389.57 | 306.76
Pageoutrun | 37598 | 63779 | 60419
pgalloc_dma | 285.27 | 532.51 | 449.75
Avg LL | 1315.38 | 1617.95 | 1862.87
working set refault (GB) | 139.52 | 376.13 | 291.71
working set activate (GB) | 34.89 | 193.69 | 118.88

## Slide 12: Priority based reclaim with memcg - Issues
Priority value of 0-10 gets added to scan size
  Scan size gets too small with per-app cgroups. e.g. cgroup priority of 10 right shifts LRU scan size by 22 at kswap priority 12
  Giving a range from -5 to +5 for cgroup priorities reduces the problem to some extent
Irrespective of the cgroup priority value, the problems with no reclaim at higher Kswapd priorities and high reclaim at lower priorities will remain depending on the size of apps
Higher amount of bulk reclaim at lower kswapd priorities due to less availability of pages at higher kswapd priority
Higher amount of IO due to thrashing
  workingset_refaults and IO has doubled
Questions to Google
  Are there any updates to the patches available in lkml along with the lmkd changes ?
  On lkml it was mentioned that no reclaim from persistent processes helped receive notifications faster. Are there any other such usecases that benefited with this approach ?
  The range of memcg priorities used by google for their tests

## Slide 13: Questions to Google
Questions to Google
  Are there any updates to the patches available in lkml along with the lmkd changes ?
  On lkml it was mentioned that no reclaim from persistent processes helped receive notifications faster. Are there any other such usecases that benefited with this approach ?
  The range of memcg priorities used by google for their tests

## Slide 14: Per app memcg – Dual LRU
Each page is linked to 2 LRUs - One global LRU and a per app memcg LRU.
Global reclaim uses the global LRU and targeted reclaim can use per memcg LRU.
Solves the problem of aging of pages, priority drop and thrashing due to tiny LRUs and helps effective reclaim of cold pages from foreground tasks.
The memcg priority patch can be integrated with this approach to achieve similar objectives.
The global reclaim path can be made aware of priority of each page chosen for “scan” using page->mem_cgroup->priority.

## Slide 15: Per app memcg – Dual LRU
This data can then be used for selectively activating/skipping pages in in the reclaim path (shrink_active_list and page_check_references).
For e.g. referenced foreground pages can be given more chance to stay on LRU and background pages can be reclaimed more.
As a useful side effect of skipping warm foreground pages and aggressively reclaiming background pages, the vmpressure will scale up when background pages on LRU tends towards zero.
Thus the default vmpressure mechanism could be effectively used by lowmemorykiller.
The detailed heuristics on selecting pages based on memcg priority is worked upon.

## Slide 16: Backup

## Slide 17: Priority based reclaim with memcg – Seq. LL
App Name | Base No MemCG |  | MemCG Priority (FG 10, Root 9, BG 0) |  | MemCG Priority (FG 5, Root 4, BG -5) | 
org.videolan.vlc/.gui.MainActivity | 565.3 | 652 | 577.2 | 636 | 583.7 | 644
com.google.android.apps.translate/.TranslateActivity | 595.7 | 629 | 592.4 | 662 | 610 | 835
com.fingersoft.hillclimb/com.fingersoft.game.MainActivity | 1370.3 | 1902 | 1345.1 | 1498 | 1624.1 | 1926
com.android.chrome/org.chromium.chrome.browser.ChromeTabbedActivity | 253.8 | 287 | 268.3 | 297 | 252.4 | 410
com.android.vending/com.google.android.finsky.activities.MainActivity | 499.8 | 517 | 507.3 | 541 | 492.7 | 528
com.google.android.apps.maps/com.google.android.maps.MapsActivity | 1112 | 1203 | 1093.2 | 1141 | 1136.8 | 1278
com.imangi.templerun2/com.imangi.unityactivity.ImangiUnityNativeActivity | 581.3 | 703 | 601.4 | 715 | 604 | 738
com.twitter.android/.dialog.PhoneVerificationDialogFragmentActivity | 3342.4 | 4111 | 5666.3 | 15471 | 7034.5 | 8538
com.google.android.youtube/com.google.android.apps.youtube.app.WatchWhileActivity | 2481.3 | 4165 | 2541.3 | 9198 | 5019.7 | 8689
com.vectorunit.purple.googleplay/.Purple | 3828.1 | 5821 | 8566.4 | 24091 | 7368 | 14573
com.google.android.gm/.ConversationListActivityGmail | 1182.9 | 1381 | 1159 | 1301 | 1245.1 | 1410
com.halfbrick.jetpackjoyride/com.halfbrick.mortar.MortarGameActivity | 1499.1 | 2060 | 1303 | 1513 | 1510.1 | 1930
com.facebook.katana/.LoginActivity | 1845.7 | 2403 | 1674.67 | 2773 | 2126.22 | 2674
com.imangi.templerun/com.imangi.androidactivity.ImangiAndroidActivity | 499.9 | 746 | 462.5 | 754 | 545.5 | 818
com.google.android.music/com.android.music.activitymanagement.TopLevelActivity | 2275.2 | 3497 | 1899.8 | 2141 | 2118.4 | 2354
com.google.android.apps.magazines/com.google.apps.dots.android.newsstand.home.HomeActivity | 928.4 | 1227 | 871.2 | 1185 | 1050.5 | 1305
com.king.candycrushsaga/.CandyCrushSagaActivity | 845.2 | 2298 | 801.8 | 986 | 719.5 | 1056
com.kiloo.subwaysurf/com.kiloo.unityutilities.UnityPluginActivity | 725.1 | 926 | 733.4 | 1059 | 950.7 | 1090
com.lenovo.anyshare.gps/com.lenovo.anyshare.activity.MainActivity | 932 | 1072 | 928.8 | 1128 | 1148 | 1478
com.opera.browser/com.opera.android.BrowserActivity | 944.2 | 1455 | 766 | 1329 | 1117.5 | 1850
Avg LL and Max LL | 1315.38 | 37055 | 1617.95 | 68419 | 1862.87 | 54124

## Slide 18
Use for Qualcomm Technologies, Inc.