## Slide 1: Migration of ION/KGSL pages
Linux Kernel Team

## Slide 2
ION and KGSL allocations are non-movable allocations.
Non-movable pages – Pages that can’t be moved by page migration facility of Linux kernel.
Page migration – Technique on which features like “memory compaction” works to create higher order (i.e. big contiguous) pages of memory by migrating movable pages.
Problem – Presence of non-movable ION/KGSL pages in large numbers causes memory compaction to fail. Results in lack of higher order pages.
ION/KGSL pages are non-movable because of their usage by external clients like GPU.
The Problem

## Slide 3
Making ION/KGSL pages movable.
There is a feature available in Linux (non-lru page migration support) which can be used to make these pages movable.
This needs support driver support
  To register for non-lru page migration infrastructure.
  To perform steps so that a parallel DMA by client on movable buffers work seamlessly.
Solution

## Slide 4
The driver generates an anonymous inode and registers 3 address_space operations – isolate_page, migratepage and putback_page. VM invokes these driver callbacks during page migration.
  isolate_page – driver can take necessary steps so that a page migration from another CPU won’t pick this page.
  migratepage – A new page is provided to the driver to copy the old page to.
  putback_page – Invoked only if migratepage fails to remove isolation.
  Whenever the driver allocates pages, the page->mapping is set to address_space of the anonymous inode, thus VM knows the callbacks to be invoked for migration.
How it works

## Slide 5
The page copied in migratepage may be accessed in parallel by a client say GPU, thus certain steps need to taken in the migratepage callback.
Here is a sample depiction of steps in migratepage()
  From the old page find the SMMU mapping. Call into SMMU driver and replace the SMMU PTE with a special MIGRATION_PTE, TLB invalidate for VA. The MIGRATION_PTE will let the fault handler know that a migration is in progress.
  Move to new page. Set the new PTE.
  During this process if GPU accesses the page, a SMMU fault triggers and driver handler will be invoked.
  The fault handler sees MIGRATION_PTE and waits for migration to complete.
  The fault handler resumes the faulted transaction.
How it works

## Slide 6
http://opengrok.qualcomm.com/source/xref/kernel_msm-4.9/kernel/Documentation/vm/page_migration - Description of non-lru migration
http://opengrok.qualcomm.com/source/xref/kernel_msm-4.9/kernel/mm/zsmalloc.c#1962 – For reference, implementation of non-lru migration for zram.
Related documents

## Slide 7
Use for Qualcomm Technologies, Inc.