## Slide 1: Agenda
What is SSR?
What triggers a SSR.
Notifications.
High Level Sequence.
When APSS crashes!!!
SFR & Ramdumps.
Userspace Interfaces.
References.

## Slide 2: What is SSR?
SSR is a feature to restart one subsystem by another subsystem without resetting the SOC.
In older implementations, if any of the SS panics or goes unresponsive, the SOC needs to be reset. To avoid this, SSR mechanism is implemented where APSS SS takes care of restarting the crashed SS, hence enhancing the user experience.

## Slide 3: What triggers SSR?
Fatal error on subsystem.
  Uses SMP2P interrupt
Watch dog interrupt
  Each SS has hard interrupt line to APPS for WDOG interrupt.

## Slide 4: Notifications
Local kernel notifications.
Remote notifications.

## Slide 5: Local Notifications
Notifications send across Linux kernel targeting interested drivers on APPS side.
This allows dependent drivers to cleanup their states.

## Slide 6: Local Notification Driver
drivers/soc/qcom/subsystem_notif.c
Simple driver that allows a driver to register for subsystem notifications, provides APIs to the subsystem restart framework to send out those notifications to the drivers.
One can register for notifications before the subsystem driver itself has probed.
Uses SRCU notification, notifiers run in thread context.
Blocking, no timeout. Shouldn’t delay the subsystem restart process unreasonably.

## Slide 7: Remote notifications - Sysmon
A client-server protocol to allows subsystems to communicate subsystem-state to each other.
Client runs on the apps processor, servers on all other subsystems.
Example use case: When the modem crashes, the LPASS/ADSP subsystem driver informs the ADSP that the modem has crashed via the sysmon API.
Uses QMI interface as the communication transport protocol.

## Slide 8: Notifications Types
SUBSYS_BEFORE_SHUTDOWN
SUBSYS_AFTER_SHUTDOWN
SUBSYS_BEFORE_POWERUP
SUBSYS_AFTER_POWERUP
SUBSYS_RAMDUMP_NOTIFICATION
SUBSYS_POWERUP_FAILURE
SUBSYS_PROXY_VOTE
SUBSYS_PROXY_UNVOTE
SUBSYS_SOC_RESET

## Slide 9: High level Sequence
Subsystem indicates a fault via a fault indicator interrupt
Subsystem driver or subsystem framework intercepts the error and invokes subsystem_restart
Notifications are sent to drivers before shutting down the subsystem
Subsystem is shutdown.
Memory dump of the subsystem is taken if necessary.
Notifications are sent to drivers after shutting down and before powering up the subsystem
Subsystem is powered up.

## Slide 10: When APSS crashes!!!
When the apps processor crashes - due to linux driver/kernel crashing - or for any other reason (unhandled page fault for ex.), other processors in the system need to be informed:
  - So that they can cleanly shutdown and flush their caches, dump debugging information etc.
Each subsystem driver registers a crash_shutdown callback, that is invoked in a panic notifier by the subsystem restart framework.
Regular shutdowns may be communicated at a higher level (QMI etc).

## Slide 11: Force Stop/Stop ACK
Force stop
  SMP2P gpio to set the SMP2P bit that tells the subsystem to stop execution immediately. Used in the crash_shutdown callbacks by subsystem drivers to tell subsystems to flush caches, cleanup etc. during an apps panic.
Stop Ack
  SMP2P gpio interrupt that is triggered when a subsystem acknowledges the receipt and processing of the Force stop bit.

## Slide 12: Components
Subsystem Restart framework
  subsystem_restart.c – The framework implementation that performs SSR sequences and monitors some fault/error indicators (SMP2P interrupts).
Subsystem Driver (eg: pil-q6v5-mss.c, subsys-pil-tz.c)
  A driver that represents the subsystem on the apps processor. Contains shutdown/powerup functions, error handlers etc. Registers with the subsystem_restart and PIL frameworks.
Subsystem notification driver
  Drivers register with this notification driver to receive notifications when a subsytem is restarted.
Notes: •Example use case for sysmon: When the modem crashes, the LPASS/ADSP subsystem driver informs the ADSP that the modem has crashed via the sysmon API.

## Slide 13: SFR and Ramdumps
To aid debugging, subsystem drivers may print out the reason for a subsystem’s crash in the kernel log – this reason is populated by the crashing subsystem. Known to drastically reduce debugging time.
Subsystem drivers can use the ramdump API (a miscdevice) to dump their subsystem’s memory to the filesystem. We have now switched to dumping the ELF sections instead of hardcoding memory addresses that need to be dumped.
Memory dumps go into files residing on the HLOS filesystem.
TZ needs to unlock XPUs to allow ramdumps.
To enable ramdump collection:
  echo 1 > /sys/module/subsystem_restart/parameters/enable_ramdumps

## Slide 14: Userspace Interfaces
/sys/module/subsystem_restart/parameters
  enable_debug -> timeout for error_ready interrupt is bypassed
  enable_ramdumps -> enables ramdump collection if a subsystem is restarted
  disable_restart_work -> Disables SSR. If enabled, do not trigger ssr
  max_history_time = 3600
  max_restarts -> Default 0 -> Panic is triggered if max_restarts expired in max history time.
/sys/bus/msm_subsys/devices/subsys*/
  name -> name of the subsystem
  state -> online/offline status
  crash_count -> number of times the subsystem has crashed
  restart_level -> system/related status
  system_debug -> Debugging purpose: Set to trigger panic to collect system ramdump on watchdog bite
  firmware_name -> write/read the firmware name so that clients can use different firmware loading

## Slide 15: Interfaces to load/unload a Subsystem
Kernel space API:
  Method 1. subsystem_get(“subsystem name”)/subsystem_put()
  Argument is the name of the subsystem.
  eg:- subsystem_get(“modem”)
User Space:
  Method 2. Write “get” or “put” on sysfs file
  eg:- echo get > /sys/kernel/debug/msm_subsys/modem
  Method 3. Open or close device file
  eg-: /dev/subsys_modem

## Slide 16: References
go/subsystemrestart