## Slide 1: ARMv8 Memory Model
Shiraz Hashim

## Slide 2: ARMv8 Memory Model
Separate TTBR register for user and kernel
Selection based on higher bits of the virtual address
Maximum 48-bit virtual address for each TTBR
IPA supports 48 bits on same basis
Maximum 48-bit physical address
Upper 8 bits of the address can be configured for Tagged Pointers
Address Space

## Slide 3: ARMv8 Memory Model
Exception levels above EL0 manage their own translation context, Translation base address, control registers, exception syndrome etc
EL0 translation managed by EL1
EL2 manages an additional stage2 of translation for EL1/EL0 in the Non-secure state only
Address Space

## Slide 4: ARMv8 Memory Model
Address Space

## Slide 5: ARMv8 Memory Model
Input address size
  TCR.TxSZ fields specify the input address size
IPA address size
    TCR.IPS fields specify the Intermediate Physical Address Size
Physical address size
  The ID_AA64MMFR0_EL1.PARange field indicates the implemented physical address size
Address Space

## Slide 6: ARMv8 Memory Model
Address calculations are done using 64bit registers
supervisory software can configure the top eight address bits for use as a tag
If this is done, address bits[63:56]
  Are not considered when determining whether the address is valid
  Are never propagated to the program counter
Address Space

## Slide 7: ARMv8 Memory Model
Linux Address Space
0x0000007FFFFFFFFF
0xFFFFFFFFFFFFFFFF
0x0000007FFFFFFFFF
0x0000000000000000
0xFFFFFF8000000000
0x0000000000000000

## Slide 8: ARMv8 Memory Model
Linux Address Space
0x00000000FFFFFFFF
0x0000007FFFFFFFFF
0x0000007FFFFFFFFF
0xFFFFFF8000000000
0x0000000000000000
0x0000000000000000

## Slide 9: ARMv8 Memory Model
39-bit virtual address for both user and kernel
  0000000000000000-0000007fffffffff (512GB) : user
  [architectural gap]
  ffffff8000000000-ffffffbbfffeffff (~240GB) : vmalloc
  ffffffbbffff0000-ffffffbcffffffff (64KB) : [guard]
  ffffffbc00000000-ffffffbdffffffff (8GB) : vmemmap
  ffffffbe00000000-ffffffbffbffffff (~8GB) : [guard]
  ffffffbffc000000-ffffffbfffffffff (64MB) : modules
  ffffffc000000000-ffffffffffffffff (256GB) : mapped RAM
Linux Address Space

## Slide 10: ARMv8 Memory Model
arch/arm64/include/memory.h
#ifdef CONFIG_ARM64_64K_PAGES
#define VA_BITS (42)
#else
#define VA_BITS (39)
#endif
#define PAGE_OFFSET (UL(0xffffffffffffffff) << (VA_BITS - 1))
#define MODULES_END (PAGE_OFFSET)
#define MODULES_VADDR (MODULES_END - SZ_64M)
#define FIXADDR_TOP (MODULES_VADDR - SZ_2M - PAGE_SIZE)
#define TASK_SIZE_64 (UL(1) << VA_BITS)
#ifdef CONFIG_COMPAT
#define TASK_SIZE_32 UL(0x100000000)
#define TASK_SIZE (test_thread_flag(TIF_32BIT) ? \
TASK_SIZE_32 : TASK_SIZE_64)
#else
#define TASK_SIZE TASK_SIZE_64
#endif /* CONFIG_COMPAT */
Linux Address Space

## Slide 11: ARMv8 Memory Model
Two different translation granules: 4KB and 64KB
Number of translation tables and maximum VA range:
  4KB and 4 levels => 48-bit VA
  64KB and 3 levels => 48-bit VA (top table partially populated)
  4KB and 3 levels => 39-bit VA (currently used by AArch64 Linux)
  64KB and 2 levels => 42-bit VA
Large page (block) mapping supported
  2MB and 1GB with 4KB page configuration
  512MB with 64KB page configuration
MMU Support

## Slide 12: ARMv8 Memory Model
4-level lookup, 4KB translation granule, 48-bit address
  9 address bits per level
MMU Support
2-level lookup, 64KB page/page table size, 42-bit address
  13 address bits per level
  3 levels for 48 bits of VA –top level table is a partial table
64-bit Translation table entry format

## Slide 13: ARMv8 Memory Model
4KB page configuration
  3 levels of page tables
  Linear mapping using 4KB, 2MB or 1GB blocks
64KB page configuration
  2 levels of page tables
  Linear mapping using 64KB or 512MB blocks
  AArch32 (compat) not supported because the 32-bit ABI assumes 4KB pages
SPARSEMEM support
  SPARSEMEM_VMEMMAP optimization for virtual mapping of the struct page array (mem_map)
Linux MMU Support

## Slide 14: ARMv8 Memory Model
Normal
  Bulk memory operations, R/W, R/O
Device
  Speculative reads forbidden
  Additional attributes
    Non-Gathering (nG)
      Prevents aggregation of R/W
    Non-Reordering (nR)
      Preserves access order and synchronization requirements
    Non-Early write acknowledgement (nE)
      Write can be acknowledged at the end point
Memory Types

## Slide 15: ARMv8 Memory Model
Shareability
  Non-shareable, inner shareable, outer shareable
Cacheability
  Non-cacheable, write-through cacheable, write-back cacheable
Memory Types

## Slide 16: ARMv8 Memory Model
arch/arm64/include/memory.h
/*
* Memory types available.
*/
#define MT_DEVICE_nGnRnE 0
#define MT_DEVICE_nGnRE 1
#define MT_DEVICE_GRE 2
#define MT_NORMAL_NC 3
#define MT_NORMAL 4
Memory Types

## Slide 17: ARMv8 Memory Model
Physical memory locations are accessed with mismatched attributes if all accesses to the location do not use a common definition of all of the following attributes of that location:
  Memory type, Device or Normal.
  Shareability.
  Cacheability, for the same level of the inner or outer cache
Collectively these are referred to as memory attributes.
ARM strongly recommends not to use mismatched attributes for aliases of the same location. An implementation might not optimize the performance of a system that uses mismatched aliases.
Mismatched Attributes

## Slide 18: ARMv8 Memory Model
Higher Exception level can enable EL0 access to the following:
  data cache maintenance instructions (DC CVAU, DC CVAC, and DC CIVAC)
  instruction cache maintenance instruction, (IC IVAU)
  cache type register (CTR_EL0)
  data cache zero instruction, (DC ZVA)
Cache Maintenance

## Slide 19: ARMv8 Memory Model
ISB
  flushes the pipeline in the PE
DMB
  data memory barrier
  Takes required shareability domain and required access types as arguments
DSB
  synchronizes the execution stream with memory accesses
  Takes required shareability domain and required access types as arguments
Memory Ordering

## Slide 20: ARMv8 Memory Model
Shareability Domain Argument
  Full system
  Outer Shareable
  Inner Shareable
  Non-shareable
Access Type Argument
  Read and write accesses in Group A and Group B.
  Write accesses only in Group A and Group B.
  Read access only in Group A.
Memory Ordering (DSB/DMB)

## Slide 21: ARMv8 Memory Model
arch/arm64/include/asm/barrier.h
#define isb() asm volatile("isb" : : : "memory")
#define dmb(opt) asm volatile("dmb " #opt : : : "memory")
#define dsb(opt) asm volatile("dsb " #opt : : : "memory")
#define mb() dsb(sy)
#define rmb() dsb(ld)
#define wmb() dsb(st)
Memory Ordering (DSB/DMB)