## Slide 1: Core Isolation
Pavankumar Kondeti
6/23/2017

## Slide 2: Agenda
core Isolation introduction
core Isolation API
core_ctl
upcoming requirements
References

## Slide 3: Core Isolation Introduction
Hotplug has been used as a power saving feature for a long time in QC chips
Thermal also benefits from hotplug
Hotplug is a *heavy* operation. There are instances where SoC is reset before thermal hotplugs CPUs.
All we need is to keep a CPU in the deep c-state as much as possible to save power / help thermal
Isolation is supposed to achieve this goal. Loosely based on isolcpus and cpuset.quisce features available in upstream.
hotplug vs isolation

## Slide 4: Core Isolation Introduction
When a CPU is isolated
  Migrate all timers/hrtimers except pinned timers
  Disable kernel watchdog
  Migrate all IRQs except per-cpu IRQs
  Migrate all tasks except kernel threads
  Mark this CPU as unavailable for load balancing
Any task affinity request from user space that contains only isolated CPUs is disallowed
Scheduler will not place any tasks on isolated CPUs except kernel threads
No timer/hrtimer is queued on isolated CPUs except pinned timers
CPU_DMA_LATENCY QOS for isolated CPUs return INT_MAX
What happens when a CPU is isolated

## Slide 5: Core Isolation Introduction
The CPU is marked as un-isolated
Send an IPI to participate in the load balancer right away
It is almost like waking up an idle CPU
What happens when a CPU is un-isolated

## Slide 6: Core Isolation API
int sched_isolate_cpu(int cpu)
int sched_unisolate_cpu_unlocked(int cpu)
sched_isolate() trace point gives the latency, cpu_isolate_mask
support multiple clients. core_ctl is the only active client as of today.
The calls are refcounted. The isolate and un-isolate calls must match.
Synchronized across hotplug, system suspend via cpu_add_remove_lock mutex
Client must un-isolate a CPU that is isolated earlier during hotplug. That means a CPU will never be in offline && isolate state.
/sys/devices/system/cpu/cpuX/isolate indicates the state of the CPU.
cpu_isolated_mask bitmask contains the isolated CPUs

## Slide 7: core_ctl
core_ctl manages the required number of CPUs based on the load and runnable tasks. The policy is per cluster
core_ctl hotplug the CPUs prior to 3.18 kernel and now it is moved to use core isolation
The running average of tasks metric comes from the scheduler. The period is 20 msec
The CPU load metric comes from the interactive governor. It is changed in 4.9 with EAS. core_ctl is completely free of cpufreq now.
core_ctl_set_boost() API can be used to bring in all CPUs of the BIG cluster. used by the scheduler and WLAN.
Works closely with scheduler starting from 4.4 kernel

## Slide 8: Upcoming features/requirements
Thermal started using isolation for the first time on Napali
Little cluster isolation feature is PORed for Reddragon (6 + 2). Power team also expressed interest in enabling isolation for the little cluster. Thermal may also start using it for the little cluster
SDM670/SDM845 work

## Slide 9: References
http://qwiki.qualcomm.com/quic/Kernel/sched/core_isolation
80-P0106-2 B (Core Isolation)
Refer the agile document for core_ctl tunables

## Slide 10
Use for Qualcomm Incorporated