## Slide 1: Mutex, OSQ Lock & Read-Write Semaphore

## Slide 2: Agenda
  Overview of Mutex
  Mutex Structure
  mutex_lock() approach
  mutex_unlock() approach
  Optimization-Spin on Owner
  mutex_optimistic_spin() approach
  osq_lock approach
  Mutex: RT Task Live Lock Issue
  Mutex: osq_lock queue corruption
  Overview of Rwsem
  Rwsem Count Interpretation
  down_read() approach
  down_write() approach
  up_read() & up_write() approach
  Rwsem: Missed Wakeup Issue
  Rwsem: Deadlock due to reordering of wakeup

## Slide 3: Overview of Mutex
Mutex stands for mutual exclusion
Mutual exclusion is a property of concurrency control, which is instituted for the purpose of preventing race conditions. It is the requirement that one context of execution never enter its critical section at the same time when another concurrent context of execution enters its own critical section.
Properties of Mutex:
  Only one task can hold the mutex at a time
  Only the owner can unlock the mutex
  Recursive locking is not permitted
  Only used with preemption enabled. Mutex should not be used after disabling preemption or in atomic context like interrupt (HW & SW)

## Slide 4: Mutex Structure
struct mutex {
/* 1: unlocked, 0: locked, negative: locked, possible waiters */
atomic_t count;
spinlock_t wait_lock;
struct list_head wait_list;
#if defined(CONFIG_DEBUG_MUTEXES) || defined(CONFIG_MUTEX_SPIN_ON_OWNER)
struct task_struct *owner;
#endif
#ifdef CONFIG_MUTEX_SPIN_ON_OWNER
struct optimistic_spin_queue osq; /* Spinner Osq lock */
#endif
};

## Slide 5: mutex_lock() approach
Task T1
Task T2
Mutex State
atomic_dec_return_acquire()
Count = 1
Count = 0
atomic_dec_return_acquire()
mutex_set_owner()
preempt_disable()
Count = -1
mutex_optimistic_spin()
spin_lock(wait_lock)
list_add_tail(waiter, wait_list)
set_task_state(UNINTERRUPTIBLE)
spin_unlock(wait_lock)
schedule_preempt_disabled()

## Slide 6: mutex_unlock() approach
Task T1
Task T2
Mutex State
Owner = T1, Count = -1
schedule_preempt_disabled()
mutex_clear_owner()
Owner = NULL, Count = -1
atomic_inc_return_release()
Count = 0
atomic_set(count, 1)
Count = 1
spin_lock(wait_lock)
wake_up_process(waiter->task)
spin_unlock(wait_lock)
spin_lock(wait_lock)
atomic_dec_return_acquire()
set_task_state(RUNNING)
mutex_set_owner()
spin_unlock(wait_lock)
Owner = T2, Count = 0

## Slide 7: Optimization- Spin on Owner
Try to spin for acquisition of mutex when we find that the lock owner is currently running on a (different) CPU and while we don’t need to reschedule. The rationale is that if the lock owner is running, it is likely to release the lock soon.
The mutex spinners are queued up using OSQ lock so that only one spinner can compete for the mutex.
CONFIG_MUTEX_SPIN_ON_OWNER which requires CONFIG_DEBUG_MUTEXES=n.
Executed after disabling preemption.
OSQ Lock works on building queue of per cpu osq_nodes.
struct optimistic_spin_queue {
/*
* Stores an encoded value of the CPU # of the tail node in the queue.
* If the queue is empty, then it's set to OSQ_UNLOCKED_VAL.
*/
atomic_t tail;
};
struct optimistic_spin_node {
struct optimistic_spin_node *next, *prev;
int locked; /* 1 if lock acquired */
int cpu; /* encoded CPU # + 1 value */
};

## Slide 8: mutex_optimistic_spin() approach
if (!mutex_can_spin_on_owner(lock))
goto done;
if (!osq_lock(&lock->osq))
goto done;
while (true) {
if (mutex_try_to_acquire(lock)) {
mutex_set_owner(lock);
osq_unlock(&lock->osq);
return true;
}
if (!owner && (need_resched() || rt_task(task)))
break;
}
osq_unlock(&lock->osq);
done:
set_current_state(TASK_RUNNING);
schedule_preempt_disabled();

## Slide 9: osq_lock approach
osq_lock() : queue operation
CPU0
osq_node
Tail = 1
X
X
next
prev
CPU1
CPU0
osq_node
X
next
prev
CPU1
osq_node
Tail = 2
X
next
prev
CPU0 acquired the lock & spins on owner
CPU1 is not able to acquire
osq_lock() : dequeue CPU1
CPU0
osq_node
Tail = 1
X
X
next
prev
CPU1 node unqueued as need_resched() is set and
CPU0 is holding the lock as only single spinner is allowed

## Slide 10: Mutex: RT Task Live Lock Issue
CPU0
CPU1
Mutex State
OSQ Lock
Tail = 0
CFS Task T1 : mutex_lock()
Decrements count
Owner = NULL, Count = 0
Tail = 0
CFS Task T2 : mutex_lock()
Decrements count
Acquires osq lock
Starts spinning on owner in
mutex_optimistic_spin()
Task T2 is the only task in
Runq of CPU1 so need_resched()
Will not be set on this CPU.
Owner = NULL, Count = -1
Tail = 2
CFS Task T1: mutex_lock()
Gets preempted before setting
owner
RT Task T3: mutex_lock()
Decrements count
Starts spinning in osq_lock()
Need_resched() will not be set
as this is highest priority task on
CPU0 runq
Owner = NULL, Count = -2
Tail = 1
Task T3 keeps spinning in osq_lock() on CPU0.
Task T1 will not get a chance to run resulting in
mutex never being released.
Task T2 will keep spinning on CPU1.

## Slide 11: Mutex: osq_lock queue corruption
CPU0 has acquired the lock and CPU1 is spinning in osq_node->locked loop.
CPU0
osq_node
X
next
prev
CPU1
osq_node
Tail = 2
X
next
prev
CPU2 tries to acquire osq_lock while CPU1 is dequeuing itself from osq
CPU0
osq_node
X
next
prev
CPU1
osq_node
X
next
prev
CPU2
osq_node
Tail = 3
Reordering of following stores while enqueue:
node->prev = prev;
WRITE_ONCE(prev->next, node);
Enqueue Step A: cpu1_osq_node->next = cpu2_osq_node

## Slide 12
CPU0
osq_node
X
next
prev
CPU1
osq_node
next
prev
CPU2
osq_node
Tail = 3
Dequeue Step A: cpu1_osq_node->prev->next = NULL
X
next
X
Dequeue Step B: cpu1_osq_node->next = NULL
CPU0
osq_node
X
next
prev
CPU1
osq_node
next
prev
CPU2
osq_node
Tail = 3
X
next
X
X
CPU0
osq_node
X
next
prev
CPU1
osq_node
next
prev
CPU2
osq_node
Tail = 3
X
next
X
Dequeue Step C: cpu2_osq_node->prev = cpu0_osq_node
prev
X

## Slide 13
CPU0
osq_node
X
next
prev
CPU1
osq_node
next
prev
CPU2
osq_node
Tail = 3
X
next
X
prev
X
Enqueue Step B: cpu2_osq_node->prev = cpu1_osq_node
When CPU2 starts to dequeue itself it would keep looping infinitely as cpu2_osq_node->prev->next = NULL

## Slide 14: Overview of Rwsem
Based on semaphore semantics with a twist.
Context trying to read shared data structure can acquire rwsem in read mode.
Context trying to write to shared data structure can acquire rwsem in write mode.
Multiple reader can enter critical section simultaneously.
Multiple writer can not enter critical section simultaneously.
Reader and Writer are mutually exclusive.
Two writers are mutually exclusive.

## Slide 15: Rwsem Structure
struct rw_semaphore {
long count;
struct list_head wait_list;
raw_spinlock_t wait_lock;
#ifdef CONFIG_RWSEM_SPIN_ON_OWNER
struct optimistic_spin_queue osq; /* spinner MCS lock */
/*
* Write owner. Used as a speculative check to see
* if the owner is running on the cpu.
*/
struct task_struct *owner;
#endif
#ifdef CONFIG_DEBUG_LOCK_ALLOC
struct lockdep_map dep_map;
#endif
};

## Slide 16: Rwsem Count Interpretation
Count | Interpretation
0x00000000 | rwsem is unlocked, and no one is waiting for the lock or attempting to read lock or write lock
0x0000000X | X = active_readers + readers attempting to lock (X*ACTIVE_BIAS)
0xFFFF000X | X readers active or attempting lock, with waiters for lock (X*ACTIVE_BIAS + WAITING_BIAS) 1 writer attempting lock, no waiters for lock ((X-1)*ACTIVE_BIAS + ACTIVE_WRITE_BIAS) 1 writer active, no waiters for lock ((X-1)*ACTIVE_BIAS + ACTIVE_WRITE_BIAS)
0xFFFF0001 | 1 reader active or attempting lock, waiters for lock (WAITING_BIAS + ACTIVE_BIAS) 1 writer active or attempting lock, no waiters for lock (ACTIVE_WRITE_BIAS)
0xFFFF0000 | There are writers or readers queued but none active or in the process of attempting lock (WAITING_BIAS)
0xFFFE0001 | 1 writer active, or attempting lock and waiters on queue (ACTIVE_WRITE_BIAS + WAITING_BIAS)
ACTIVE_BIAS = 0x00000001
ACTIVE_WRITE_BIAS = 0xFFFF0001

## Slide 17: down_read() approach
if (atomic_long_inc_return_acquire(count) <= 0) {
spin_lock(wait_lock)
if (list_empty(&sem->wait_list))
adjustment = RWSEM_WAITING_BIAS - RWSEM_ACTIVE_READ_BIAS
else
adjustment = - RWSEM_ACTIVE_READ_BIAS
rwsem_atomic_update(adjustment)
list_add_tail(waiter, wait_list)
spin_unlock(wait_lock)
while (true) {
set_task_state(TASK_UNINTERRUPTIBLE)
if (!waiter.task)
break
schedule()
}
set_task_state(TASK_RUNNING)
}

## Slide 18: down_write() approach
tmp = atomic_long_add_return_acquire(RWSEM_ACTIVE_WRITE_BIAS, count)
if (tmp != RWSEM_ACTIVE_WRITE_BIAS) {
rwsem_atomic_update(-RWSEM_ACTIVE_WRITE_BIAS, count)
if (rwsem_optimistic_spin(sem))
return
spin_lock(wait_lock)
list_add_tail(waiter, wait_list);
rwsem_atomic_update(RWSEM_WAITING_BIAS, count)
set_current_state(TASK_UNINTERRUPTIBLE)
while (true) {
if (rwsem_try_write_lock(count, sem))
break
spin_unlock(wait_lock)
do {
schedule();
set_current_state(TASK_UNINTERRUPTIBLE)
} while ((count = sem->count) & RWSEM_ACTIVE_MASK)
spin_lock(wait_lock)
}
set_current_state(TASK_RUNNING)
list_del(waiter)
spin_unlock(wait_lock)
}

## Slide 19: up_read() & up_write() approach
tmp = atomic_long_dec_return_release(count)
if (tmp < -1 && (tmp & RWSEM_ACTIVE_MASK) == 0)
rwsem_wake()
up_read()
up_write()
if (atomic_long_sub_return_release(RWSEM_ACTIVE_WRITE_BIAS, count) < 0)
rwsem_wake()
rwsem_wake()
if (rwsem_has_spinner()) {
smp_rmb();
if (!spin_trylock(wait_lock))
return
goto locked
}
spin_lock(wait_lock)
locked:
if (!list_empty(wait_list))
rwsem_do_wake()
spin_unlock(wait_lock)
}

## Slide 20: Rwsem: Missed Wakeup Issue
If a spinner is present, there is a chance that the load of rwsem_has_spinner() in rwsem_wake() can be reordered with respect to decrement of rwsem count in __up_write() leading to wakeup being missed.
spinning writer up_write caller
--------------- -----------------------
[S] osq_unlock() [L] osq
spin_lock(wait_lock)
sem->count=0xFFFFFFFF00000001
+0xFFFFFFFF00000000
count=sem->count
MB
sem->count=0xFFFFFFFE00000001
-0xFFFFFFFF00000001
RMB
spin_trylock(wait_lock)
return
rwsem_try_write_lock(count)
spin_unlock(wait_lock)
schedule()
Reordering of atomic_long_sub_return_release() in __up_write() and rwsem_has_spinner() in rwsem_wake() can cause missing of wakeup in up_write() context. In spinning writer, sem->countand local variable count is 0XFFFFFFFE00000001. It would result in rwsem_try_write_lock() failing to acquire rwsem and spinning writer going to sleep in rwsem_down_write_failed(). The smp_rmb() will make sure that the spinner state is consulted after sem->count is updated in up_write context.

## Slide 21: Rwsem: Deadlock due to reordering of wakeup
Waiting reader up_write/up_read caller
--------------------- -----------------------------
spin_lock(wait_lock)
rwsem_atomic_update(adjustment)
list_add_tail(waiter, wait_list)
spin_unlock(wait_lock)
set_task_state(TASK_UNINTERRUPTIBLE)
schedule()
waiter = list_entry(wait_list)
tsk = waiter->task
smp_mb();
wake_up_process(tsk)
waiter.task != NULL
schedule()
waiter->task = NULL
Reordering between loads in
wake_up_process() &
waiter->task = NULL